The IF Statement

You can think of the If statement block as a question that requires a True or False answer. The answer determines which section of code your program will execute. Since computers only work with numbers, you frame the question as a conditional equation that will result in either 0 for False or non-zero for True.

The If statement has the following formats.

If <expression> Then Do something[:Do something]

The <expression> is the question that requires a True or False answer. If the answer is True, i.e. not False, then the code following the Then is executed. If the answer is False then the next line of code is executed.

You can execute more than one statement after the Then if you separate the statements with a colon. All of the statements must be on the same line. An easier format is to use the IF code block, as shown below.

If <expression> Then
    Do something 1
    Do something 2
    ...
End If

In this format if the answer is True then the code block following the Then is executed, starting with statement 1 and executing all statements until the End If is reached. The program will then start executing code after the End If. If the answer is False, the code in the code block is skipped and the code following the End If is executed.

If <expression> Then
    Do something
    ...
Else
    Do something Else
    ...
End If

In this format if <expression> is True then the code following the Then is executed. If the answer is False then the code following the Else is executed. In this format you can address both the True and False answers of the <expression>.

If <expression> Then
    Do something
ElseIf <expression> Then
    Do something
End If

In this format if <expression> is True then the code following the Then is executed. If the answer is False then the ElseIf is executed. If the ElseIf is True, the code following the Then (of the ElseIf) is executed, otherwise the code following the End If is executed. You can have as many ElseIf statements as you need to fully cover the range of questions you need to ask.

If <expression> Then
    Do something
ElseIf <expression> Then
    Do something
Else
    Do something Else
End If

This format is a combination of all the other formats. If <expression> is True then the code following the Then is executed. If the answer is False then the ElseIf is executed. If the ElseIf is True, the code following the Then (of the ElseIf) is executed, otherwise the code following the Else is executed.

This format enables you to ask a series of questions and if the answer is False to all the questions, you can take a default course of action based on the Else block.

As you can see you can frame the question in a number of ways and then execute the code based on a number of answer combinations. This gives you a lot of flexibility in how to both frame a question and what to do based on the answers.

The <expression> is the question that needs an answer and you frame the question using logical operators.

You can mix arithmetic and logical operators, as well as parenthesis, within an If statement. The compiler evaluates the conditional statements from left to right, taking into account the precedence of the operators. For example, all of the following code snippets are legal If statement constructs.

If var1 = 5 Then
If (var1 = 5) And (var2 < 3) Then
If (var1 + 6) > 10 Then

You will notice that parenthesis are used to group the different parts of the expressions. You should use parenthesis to make sure that you are executing logical portions of the expressions. The expression must ultimately resolve to either True or False, even if you are using arithmetic operators within the expression.

Using Bitwise Operators in an If Statement

Remember that the operators And, Or and Not are bitwise operators. That is, they return a value based on the bitwise operation that they perform. You should take care when using bitwise operators within an If statement to make sure that the result will evaluate correctly.

Take the second code snippet listed above.

If (var1 = 5) And (var2 < 3) Then

If var1 equals 5, the compiler will return True, or -1 for the expression. If var2 is less than 3 then the compiler will return True or -1 for this expression. The compiler will then evaluate the And operator with -1 And -1 returning -1. Since -1 is non-zero, or True, the code following the Then will be executed.

If either of the statements within the parenthesis evaluate to 0, then And will return 0, which is False, and the code following the Then clause will be skipped. When using bitwise operators you should frame the conditional expressions on either side of the bitwise operator so that they return either True or False. This will give you consistent results in your evaluations.

The Not Problem

The Not bitwise operator can be a problem in an If statement. You may be used to writing If Not var Then, with Not performing a logical, rather than a bitwise operation. In FreeBASIC Not performs a bitwise operation, not a logical operation.

If var were to contain the value of 3, then Not 3 is -4, which will be regarded as a True result and the code following the Then will be executed, which is probably not what you wanted. Instead of writing If Not var Then, you should write If var <> 0 Then.

Overlapping Conditions

When using compound conditions care must be taken to ensure that the conditions do not overlap. In most cases overlapping conditions will produce unpredictable results. Each condition must produce a unique result, and the combination of the individual results, must itself express a unique result. This is very important in If-ElseIf constructs; an overlapping condition within an If-ElseIf block may execute the wrong code at the wrong time.

Nested If Statements

At times it may become necessary to nest If statements in order to better describe the decision making process of the evaluation. While the If statement can handle multiple arguments within an expression, there are times when you may want to incrementally check for certain ranges of values which you can do using a nested If block.

If <expression> Then
    <statement>
    ...
    If <expression> Then
        <statement>
        <statement>
        ...
    End If
End If

It is important to close each block properly with an End If when opened by an If to avoid compiler or logical errors. Compiler errors are fairly easy to fix, while logical errors can be tricky to track down and correct. The best way to make sure you are closing the blocks properly is to indent the nested If statements and then indent the matching End If statements at the same level as the If. In the example above, the indentation tells you at a glance which End If goes with which If.

The IIF Function

The Iif, or "immediate If" function returns one of two numeric values based on an expression. You can think if the Iif function as an in-line If statement that acts as a function call.

Value = IIf(<expression>, numeric_value_if_true, numeric_value_if_false)

Iif can be used as a standalone function or inside other expressions where you do not want to split the expression to insert an If statement. The numeric values can be literal values, variables or numeric function calls. The limitation of the function is that it will only return a numeric value, not a string value, however you can work around this limitation by using pointers.

The Iif statement will evaluate both the True and False conditions so you need to take care that you do not perform an illegal operation such as divide by zero in a condition, even if that condition is not returned from the function.

Framing the Question

The If statement is a powerful tool, but you need to make sure that you are framing the question, that is the expression, correctly. Each expression must resolve to True or False, with True always executing the code following the Then.

When writing an If statement you must ask yourself, does this expression resolve to True or False? This is especially true for compound expressions that have a number of terms within the expression. Each term must resolve to True or False and the sum of the terms must resolve to True or False. If there is any doubt that a compound expression is evaluating correctly, break it into nested If statements.

Checking For Range Values

Often times you will need to check for a range of values within an If statement, and in order for the compiler to evaluate the range condition correctly, you must frame the expressions correctly. There are basically two type of range expressions: exclusive and inclusive ranges. Exclusive range expressions exclude a range of values. Inclusive range expressions include a range of values. Each has a particular format that must be followed for proper evaluation.

Excluding a Range of Values

Suppose that you have a range of values and you want to do something special if the value is less than or equal to 1 or the value is greater than or equal to 10. To put this another way, you want to exclude the numbers 2 through 9 from the special action.

You can frame this as a question that can then be translated into code.

Is the value a number less than Or equal To 1 Or a number greater than Or equal To 10?
If Yes, Then Do special action.
If No, Then Do standard action.

The key here is the OR. If the lower bound of the value is equal to or less than 1 OR the upper bound of the value is equal to or greater than 10 then do the special action.

If (value <= 1) Or (value >= 10) Then
    do_special
Else
    do_standard
End If

Remember that OR will return True if either condition is True. If the value is 1 or less, or the value is 10 or more, then the expression will return True and the special action will be performed.

Including a Range of Values

Inclusion is the opposite of exclusion. As you might guess, the format is similar you but you use the And operator which is the opposite of the OR operator.

Suppose you want to do something special if the value is a 5, 6 or 7. That is you want to include these numbers within your range expression. Again, you can start by asking a question.

Is the value a number between 5 And 7 (inclusive)?
If Yes, Then Do special action
If No, Then Do standard action

Here you want to include the numbers 5, 6, 7 for consideration. That is if the value is 5 or greater AND the value is 7 or less then do something special. This translates to the following code snippet.

If (value >= 5) And (value <= 7) Then
    do_special
Else
    do_standard
End If

Remember that the And operator will only return True if both operands return True. If value is 6, 6 is greater than 5 and 6 is also less than 7, so both statements are True and the expression evaluates to True.

Editors Note: See also AndAlso and OrElse

Last Reviewed By Sancho3, February 06, 2018

The Select Case Statement
Written by rdc

The Select Case block can be viewed as an optimized If-ElseIf ladder, and works in much the same way. The standard Select Case can use any of the standard data types for <expression> and the specialized Select Case As Const format is optimized for integer values.

This code snippet shows the syntax of the standard select case. Expression is usually a variable which can be of any of the standard data types, or individual elements of a Type or array.

Select Case <expression>
    Case <list>
        <statement>
        <statement>
        ...
    Case Else
        <statement>
        <statement>
        ...
End Select

The <list> clause of the Case statement can be any of the following formats.
Case <value>: Value is one of the supported data types or an enumeration.
Case <value> To <value>: Specifies a range of values.
Case Is <operator> <value>: Operator is any of the logical operators.
Case <value>, <value>, ...: List of values separated with commas.
Case <variable>: A variable that contains a value.

The following snippet illustrates how these different formats may be used in a program.

Case 47

Case 47 To 59

Case Is > 60

Case 47, 48, 53

Case keycode

The Select Case As Const is a faster version of the Select statement designed to work with integer expressions in the range of 0 to 4097.

Select Case As Const <integer_expression>
    Case <list>
        <statement>
        <statement>
        ...
    Case Else
        <statement>
        <statement>
        ...
End Select

The <list> statement formats for the Select Case As Const are limited to values or enumerations of values. That is, the operator expressions are not allowed within a Case As Const.

When a Case block is executed, the statements following the Case keyword up to the next Case keyword (or End Select) will be executed. Only one block of statements within a Case will execute at any one time. If a Case Else is present, then the statements within the Else block will execute if no Case matches the <expression> portion of the Select statement. The following program illustrates using the Select Case statement block.

'Ascii code of key press
Dim As Integer keycode

'Loop until esc key is pressed
Do
    keycode = Asc(Inkey)
    Select Case As Const keycode
        Case 48 To 57
        Print "You pressed a number key."
        Case 65 To 90
        Print "You pressed an upper case letter key."
        Case 97 To 122
        Print "You pressed a lower case key."
        End Select
        Sleep 1
Loop Until keycode = 27 '27 is the ascii code for Escape

End

In the program, when you press a key, the value is translated to a number using the Asc function. Since this will always be an integer value that is less than 4097 (since ascii character codes range from 0 to 255), the Select Case as Const format is used.

The compiler will check the value of keycode against the Case ranges to see if the block should execute. If keycode falls within a particular range, the Print statement will execute, and then the flow of the program will continue with the next line following the End Select. If keycode doesn't match any Case range, then the program will continue with the next line following the End Select.

A Select Case can usually be translated from an If-Elseif ladder. To illustrate this, the previous program is shown below as an If-ElseIf ladder.

'Ascii code of key press
Dim As Integer keycode

'Loop until esc key is pressed
Do
    keycode = Asc(Inkey)
    If (keycode >= 48) And (keycode <= 57) Then
        Print "You pressed a number key."
    ElseIf (keycode >= 65) And (keycode <= 90) Then
        Print "You pressed an upper case letter key."
    ElseIf (keycode >= 97) And (keycode <= 122) Then
        Print "You pressed a lower case key."
    End If
    Sleep 1
Loop Until keycode = 27 '27 is the ascii code for Escape

End

If you compare the two programs, you can see that the logic is quite similar, however the Select Case is much more readable and understandable than the If-ElseIf ladder.

Last Reviewed by Sancho3 on February 06, 2018

Looping Statements
These statements are used for executing a block of statements repeatedly. Within a statement block, the loop can be prematurely re-executed using the CONTINUE keyword, or broken out of using the EXIT keyword. Whether the loop is terminated by the condition or with the EXIT keyword, execution always begins at the first statement after the block.

WHILE..WEND
Executes a block of statements while some expression evaluates to true (the condition). The expression is evaluated and checked before the block of statements is executed.

FOR..NEXT
Like WHILE..WEND, but more suited to loop a certain number of times. This loop initializes a so-called iterator with an initial value that is checked against a test expression. If the iterator compares less than or equal to the test expression (the condition), the block of statements is executed and the iterator gets incremented. The loop can also be setup so that the iterator gets decremented after every loop, in which case it is compared greater than or equal to the test expression. Iterators can be numeric data types like INTEGER or DOUBLE, or user-defined types. User-defined types must implement operator for.

DO..LOOP
The most versatile of the looping control flow statements, this loop can execute a block of statements while or until an expression evaluates to true (the condition). It can also delay the checking of the expression until after the block has executed the first time, useful when a block of statements needs to be executed at least once. Finally, this loop can have no condition at all, and merely loop indefinitely.